## Slide 1
475 Aviation Blvd., Suite 120
Santa Rosa, CA 95403
(877) NO-TELCO
www.broadlink.com
INFORMATION CONTAINED HEREIN IS OWNED AND COPYRIGHTED BY BROADLINK COMMUNICATIONS, INC. 2002
ANY REDISTRIBUTION WITHOUT THE WRITTEN CONSENT OF BROADLINK IS A VIOLATION OF COPYRIGHT LAW
Rev.02.12.02
Unlicensed Wireless Networks:
Transitioning from Private Network
to Outdoor Public Access
February 12, 2002
10:45 - 11:30 am
Tim McAllister, EVP, CTO & Co-founder

## Slide 2: Relevant Background
Working on WBA solution since 1994
Deployed WBA network in early 1996
Ran into several management, security & capacity issues early
Seeded investment in wireless broadband equipment company 1998
Low-cost CPE uses 802.11 cards & BLNK software
Presently wholesaling WBA to EarthLink
Expanding into new markets (2Q’02)

## Slide 3: Overview
Natural Migration
  Use of low-cost WLAN equipment in Public broadband access networks
Major concerns
Solutions available today
Limitations of available solutions
Solutions that work

## Slide 4: Natural Migration of WLAN to Broadband WAN
Availability of cable and DSL still limited
Pent-up demand for broadband access
Lowest cost solution
  Price dropped over 300% in two years
Standards-based platform works (802.11b)
  Working technology supported standard
  Major chip manufacturers and developers increased production and volume shipped

## Slide 5: Major Concerns w/ WLAN in Outdoor Public Wireless Broadband Access
Scalability
  WLANs are Ethernet-based (Ad Hoc networking); QoS-limited; Capacity Limited
Security
  LAN – “Listen, before talk”, prone to eavesdropping and theft of service
  WEP – Compromised by UC Berkeley & University of Maryland
  802.11x standard not flexible for open-access provisioning
  End-User Customer premise security?
Management
  Plug’n’play transparent provisioning?
  Open-Access enabled for multiple ISPs?
  Remote firmware updates, visibility and user management
Outdoor Range/RF propagation
  WLAN equipment made to be used w/in 1K’

## Slide 6: WLAN’s Issues with Scalability
Peer-to-peer networking “Ad Hoc”
  QoS-Limited – “listen, before talking” Ethernet protocol w/ no mechanism for prioritization
  Capacity Limited – Ethernet protocol inefficiencies significantly limit capacity (11 Mbps to 4-5 Mbps net)

## Slide 7: WLAN’s Issues with Security
“Listen, before talk” WLAN Ethernet protocol
  Ethernet networks (Cable modem and wireless LAN networks) are “listen, before talk” protocol-based
  If your neighbor is “listening” while your “talking”, then eavesdropping can take place!
WEP Encryption (40- & 128-bit)
  Documented hack developed by UC Berkeley & University of Maryland
Theft of Service
  IP and MAC address spoofing
  Like cell phone cloning only easier
  Duplicate IPs will cause network confusion and result in loss of service
End-User Customer premise security
  Firewall & secured bridged connections
802.1x standard
  not flexible for open-access provisioning

## Slide 8: Issues w/ Off-the-Shelf Security Solutions
Route all customers
  Not scalable - ISPs do not use routing to segment customer traffic in local access networks (use of PPPoE, ATM/PVCs, Frame relay, Bridged is prevalent)
Implement WEP (40- or 128-bit)
  Implementation has been fully exploited by Cal-Berkeley & University of Maryland studies 2001
Implement VPN (IPSec, etc.)
  Difficult to implement
  Causes large overhead that affects the user’s performance
Implement User Authentication via Radius
  Standards-based support waiting for latest release of 802.1x
  Still not flexible for Open-Access of public network

## Slide 9: WLAN Issues w/ Management
Management
  Plug’n’play transparent provisioning?
  Open-Access enabled for multiple ISPs?
  Remote firmware updates, visibility and user management

## Slide 10: WLAN Issues w/ Outdoor Range
Outdoor Range/RF propagation
  WLAN equipment made to be used w/in 1,000’
  ACK timing windows are exceeded causing wireless transmission contention and collisions (layer2 packet loss)

## Slide 11: Scalable and Secure Solutions
Address Scalability
  Manage bandwidth (layer 2/3, not radio), rate-limit to meet DSL-like service and prioritize packets
  Implement and manage MPLS as it becomes available
Security
  Manage security via hardware addresses and monitoring
  Enhance the WEP key management system
  Leverage what works 802.11x, when it works and leave the rest
  Manage the customers CPE-based firewall and business-grade connections
Management
  Provide ISPs Plug’n’play transparent provisioning
  Provide an Open-Access network enabled for multiple ISPs
  Remote firmware updates, visibility and user management
Outdoor Range/RF propagation
  Use standard-based equipment that can be configured to ignore the ACK timing windows (e.g., Cisco BR350s)

## Slide 12: Secure & Scalable Network Architecture

## Slide 13: Real World Results
Scalability
  Well over 200 remote stations being served via 1 BR352 (sector)
  Spot throughput over 2.8 Mbps – downstream & 1.7 Mbps – upstream
Security
  Have continuous AirSnort and WEP-Hack testing to validate security of user data
Management
  ISP partners (ELNK, Sonic.net, etc.) using tools for tier 1 support
  Support multiple ISPs in each market
Outdoor Range/RF propagation
  Depending on terrain achieving consistent connections between 1.5 miles and 4 miles
  Early testing of CPE-based, low-cost, high-speed 802.11 repeater (micro-cell coverage) to mitigate line-of-sight issues

## Slide 14
CONFIDENTIAL / PROPRIETARY INFORMATION NOT TO BE DISSEMINATED OR DISCUSSED
WITH ANY OTHER PARTIES; WITHOUT THE PRIOR WRITTEN CONSENT OF BROADLINK
Rev.02.12.02
Contact Information:
Tim McAllister, EVP, CTO & Co-founder
tim@broadlink.com